## Slide 1
Presented By: Alan Devkota
ECE 601
Feb 15, 2023
Department of ECE, University of Houston
Houston, TX, USA

## Slide 2
Transformer Neural Network
Self-Attention
Self-Attention
Cross-Attention
Model: Stack of encoder/ decoder blocks
Usually 3-Stage processing procedure: Linear transformation, Multi-head Attention and Feed Forward
Key Structure: Self-attention

## Slide 3
Self-Attention Mechanism
Self-Attention can be understood from a graph perspective.
Each token in the sequence could be regarded as a vertex.
Each directed edge represents the attention connection from vertex a to b, and edge weight represents attention weight
We can update each vertex’s feature by aggregating the information from its neighbors.
I like ECE Seminar

## Slide 4
Motivation
Self-Attention Cost
Quadratically scaled complexity of self-attention  Bottleneck of executing long sequences
>73% of total execution time with a sequence length of 4096, 8.65GB peak memory usage under 32-bit floating point operation
Therefore, it is critical to reduce the cost of self-attention blocks.

## Slide 5
Motivation
Repetition of the value “0” in weight or activations allows elimination of unnecessary computations.
Although GPUs are highly optimized in non-sparse dense matrix multiplication, they may not be efficient in reaping the full benefits of sparse matrix multiplication
Different layers of a neural network exhibit sparsity in unique ways, which necessitates specialized hardware due to variations in the computation nature.
Sparsity
I like ECE Seminar
Self-Attention have many weak connections that contributes very little to the final output of the feature aggregation!!

## Slide 6
Only very few attentions have weight value larger than 0.005
Model can achieve on-par accuracy while running on pruned sparse attention graph, which much reduced memory and computation
Self-Attention have many weak connections that contributes very little to the final output of the feature aggregation!!
Opportunity: Dynamic Sparsity in Attention Graphs
Notes: Attention weight matrix is dynamically changing depending on input sequence as well as different self-attention heads.
Attention sparsity  Dynamic

## Slide 7
Challenges
How to locate weak attention connection?
(Compute A, Take A as a reference  compare and select only important ones.)
Requires computing the complete attention matrix!!
Notes: Compute and prune method.
Some Redundancy

## Slide 8
Challenges
How about introducing the sparsity before Q * K’ to obtain most computation/ memory reduction?
(Detect and Omit)

## Slide 9
Challenges
How about introducing the sparsity before Q * K’ to obtain most computation/ memory reduction?
(Detect and Omit)
It requires some detection method!!
Should be light-weight, accurate and hardware-efficient (trade-off)

## Slide 10
Hardware Challenges
Should support both detection and execution
  Random projection
  Quantization/ dequantization
  Multi-precision computation
Should support sparse attention computation
  SpMM
  SDDMM
  Sparse Softmax
However, some of the sparse operators are difficult to accelerate on GPU, so they have proposed customized architecture.
Notes: Simple Dense-Dense Matrix Multiplication
Sparse Softmax
Sparse Matrix-Matrix Multiplication

## Slide 11
Solution: DOTA
Proposed top-down Software-hardware co design
  On software side  Lightweight detection n/w along with optimization of transformer model
  Hardware side  Different accelerator (on top of it workload partition, token-parallel Dataflow, and computation reordering)

## Slide 12
DOTA: Dynamic Sparse Attention Algorithm
Train a lightweight detection n/w to help detect the weak/important connection
  Low precision and low dimension
Calculate approx. attention weight using expression
P is sparse random projection and
denote approx. weights for keys and queries
Use
to preserve or discard the attention scores
Notes: Random projection, to reduce feature implement light weight detection network to obtain estimated attention scores.

## Slide 13
DOTA: Dynamic Sparse Attention Algorithm
Joint optimization of detector and transformer model to ensure detection accuracy and final model accuracy
Notes: L_model  end-to-end model prediction loss
Lmse  mean square error between approx. attention score and actual attention score.
Lambda is hyperparameter to control the two loss.

## Slide 14
DOTA Accelerator Architecture

## Slide 15
Compute Lane
Reconfigurable Matrix Multiplication Unit – Multi-precision computation
SRAM Buffer
Multi-Function Unit – Adder tree for random projection, (De)Quantization Unit, Exp/Div for Softmax function
Detector – Attention Detection, Hardware-level sparse computation scheduling

## Slide 16
Reconfigurable MMU
2D PE array
One PE architecture, row-wise reconfigurable precision
Notes: Used for all dot product operations.
Sometime more accurate, sometime light-weight

## Slide 17
Token-Parallel Sparse Attention
Naïve way – compute the output matrix row by row, from left to right

## Slide 18
Token-Parallel Sparse Attention
Naïve way – compute the output matrix row by row, from left to right

## Slide 19
Token-Parallel Sparse Attention
Naïve way – compute the output matrix row by row, from left to right

## Slide 20
Token-Parallel Sparse Attention
Naïve way – compute the output matrix row by row, from left to right

## Slide 21
Token-Parallel Sparse Attention
Naïve way – compute the output matrix row by row, from left to right

## Slide 22
Token-Parallel Sparse Attention
Utilize sparsity, compute output matrix in group of rows, each row from left to right

## Slide 23
Token-Parallel Sparse Attention
Utilize sparsity, compute output matrix in group of rows, each row from left to right

## Slide 24
Token-Parallel Sparse Attention
Utilize sparsity, compute output matrix in group of rows, each row from left to right

## Slide 25
Hardware Configuration
Notes: NVIDIA V100 GPU

## Slide 26
Evaluation: Model Accuracy
Comparable accuracy with dense models under 90-95% sparsity
Much better accuracy-sparsity trade-off than prior art (ELSA)
Notes: NVIDIA V100 GPU

## Slide 27
Evaluation: Speedup and Latency Breakdown
Notes: NVIDIA V100 GPU

## Slide 28
Evaluation: Energy Efficiency
Notes: NVIDIA V100 GPU

## Slide 29
Conclusion
Proposed way to leverage weak attention connection to reduce cost of self-attention mechanism
Light weight detection network and joint optimization
Unified hardware-software co-design
Speedup, energy-efficient with negligible accuracy degradation

## Slide 30
Thank you for your attention!
Questions ??
adevkota2@uh.edu